## Slide 1
A Hybrid Spectral-Matching and Deep-Learning System
for Real-Time Mineral Identification from Raman Spectra
Final Project Defense
Rahul [Surname]
Under the supervision of [Advisor Name]
May 8, 2026
Department of [Discipline] · [Institution Name]
1/14

## Slide 2
Problem & Motivation
Raman scattering produces a vibrational spectrum {(νi, Ii)}ᵢ₌₁ᴿ acting as a mineral fingerprint:
I(ν) = Σk Ak ℒ(ν; νk, γk) + B(ν) + η(ν)
ℒ = Lorentzian profile B(ν) = fluorescence baseline η = detector noise
Why automate identification?
Field instruments now exist; expert peak-matching does not scale.
RRUFF public library covers >4,000 species — manual lookup is the dominant bottleneck.
Identification reduces to estimating {(νk, Ak, γk)} from I(ν) and matching a reference library.
Domains directly affected
Geology & planetary science (Mars SHERLOC)
Cultural-heritage pigment analysis
Forensic mineralogy
Mining process monitoring
2/14

## Slide 3
Formal Problem Statement
Given
unknown query q = {(νi, Ii)}ᵢ₌₁ᴿ and reference library ℛ = {rm}m₌₁ᴹ defined on canonical grid ν* ∈ ℝP
Produce
1. Ranked list ((m₁,c₁), …, (m₅,c₅)) with confidences c(k) ∈ [0, 1]
2. Non-negative weight vector x ∈ ℝM≥₀ such that ‖Aᵗx − q̃‖₂ is minimised
where A is the row-stacked reference matrix and q̃ is the preprocessed query
Subject to
wall-clock budget τ ≤ 1 s on commodity hardware (single laptop GPU, 16 GB RAM)
Key design choices
Parameter | Value adopted | Consequence
Canonical grid range | [100, 4000] cm⁻¹, Δν = 2 cm⁻¹ | P = 1,951 channels
Library size M | 2,481 unique minerals | Synthetic-25 ∪ RRUFF-2456
Top-K | K = 5 | Aligns with expert workflow
Peak model | Lorentzian | Matches lifetime broadening of optical phonons
3/14

## Slide 4
End-to-End System Architecture
Upload
CSV
→
Preprocess
(§5)
Spectral
Matcher
1-D ResNet
Classifier
→
→
Auto
Dispatch
NNLS
Mixture
→
→
Identification
Composition
Spectral matching always runs as a deterministic safety net. The 1-D ResNet and RF classifiers enter the dispatch only if their top-1 confidence exceeds τmin = 0.55, preventing confidently-wrong out-of-distribution predictions.
4/14

## Slide 5
Preprocessing Pipeline
Given raw (ν_raw, I_raw), produce normalised q̃ ∈ ℝP on the canonical grid:
1
Linear interpolation onto ν*:
I_grid = interp(ν*, ν_raw, I_raw)
2
Cosmic-ray suppression (5-point ratio test):
Ii ↦ Ī_nbr · 𝟭[Ii / maxj Ij > ρ]
3
Savitzky–Golay smoothing:
window w = 5, polynomial order p = 3
4
ALS baseline removal:
min Σi wi(yi − zi)² + λΣi(Δ²zi)² λ=10⁵, asym. p=0.01
5
Non-negative clip + ℓ₂ normalisation:
q̃ = z / ‖z‖₂
Key insight: interpolation must precede smoothing. w_physical = w·δν — coupling SG to native step. A CSV at δν=4 cm⁻¹, w=11 gives 44 cm⁻¹ window (wider than Raman FWHM). Fix lifted Quartz top-1 confidence from 41% → 86%.
5/14

## Slide 6
Combined-Metric Spectral Matcher
For preprocessed query q̃ and reference row rm, define the combined similarity score:
s(q̃, rm) = ½ ⟨q̃, r̂m⟩ + ½ ⟨D²q̃̂, D²r̂m⟩
D² = SG second-derivative operator v̂ = (v − v̅·1) / ‖v − v̅·1‖
Cosine term
Sensitive to entire bandshape. Over-rewards minerals whose RRUFF average drifts in the same direction as the query (baseline slope).
Second-derivative Pearson term
Emphasises peak position and sharpness. Penalises flat spectral regions. Each metric vetos the other’s failure mode; equal weights from held-out grid search.
Reference matrix A = [r¹s,…,r²⁵s, r¹r,…,r²⁴⁵⁶r]ᵀ ∈ ℝ²˃⁰²×¹⁹⁵¹ (25 synthetic + 2,456 RRUFF-averaged rows) | Equal weights by held-out grid search.
6/14

## Slide 7
1-D Residual Classifier
Stage | Operation | Output shape
Stem-1 | Conv1D(k=25, s=2) → BN → GELU | (B, 32, 488)
Stem-2 | Conv1D(k=15, s=2) → BN → GELU | (B, 32, 244)
Stage 1 | 3× Pre-act ResBlock(32, k=7) | (B, 32, 244)
Down | Conv1D(k=5, s=2) → BN → GELU | (B, 64, 122)
Stage 2 | 3× Pre-act ResBlock(64, k=5) | (B, 64, 122)
Pool | Adaptive Average Pool 1D | (B, 64)
Head | FC₆₄→₅¹² → GELU → FC₅¹²→₈₅¹ | (B, 851)
Total params | 663,539 | 851 classes (min_spectra ≥ 2)
Training
Loss: CE + smooth ε=0.1 + Mixup(α=0.4)
Opt: AdamW + OneCycleLR, lr=10⁻³, wd=10⁻⁴
Aug: V=25 variants per sample
Spectral Augmentations (V = 25 per training sample)
Gaussian noise: σ ∼ U(0.002, 0.025)
Multiplicative jitter: β ∼ U(0.75, 1.25)
Wavenumber shift: Δν ∼ U{−10, +10} cm⁻¹
Polynomial baseline (deg 1–3, p=0.30, A=0.01)
Moving-avg broadening (p=0.40, w∈{2,3,4})
Spectral dropout (p=0.20, ≤4 points→0)
7/14

## Slide 8
Candidate-Restricted NNLS
Let Aᶜ ∈ ℝ|ᶜ|×P be the row selection of the reference matrix indexed by candidate set C. Solve:
x* = arg min_{x ≥ 0} ‖ Aᶜᵀ x − q̃ ‖²₂
Candidate set construction:
C = C_synth ∪ { m ∈ C_rruff : s(q̃, rm) > max_{m'∈C_synth} s(q̃, rm') }
Why restrict?
With |ℛ| = 2,481 candidates and P = 1,951 equations the full system is underdetermined (more unknowns than equations). NNLS spreads credit arbitrarily across minerals sharing a spectral peak. Restricting to ∼30 well-separated basis rows renders the system over-determined and physically interpretable.
8/14

## Slide 9
Confidence-Aware Dispatcher
Algorithm 1: AUTOIDENTIFY — selects the most confident identifier per query
Input: preprocessed query q̃, threshold τ_min = 0.55
Output: ranked top-K list, dispatch tag
1 Y ← ∅
2 m_s ← SpectralMatch(q̃); Y ← Y ∪ {(m_s[1].c, "matching", m_s)}
3 if CNN available then
4 m_n ← CNNPredict(q̃)
5 if m_n[1].c ≥ τ_min then Y ← Y ∪ {(m_n[1].c, "cnn", m_n)}
6 if RF available then
7 m_r ← RFPredict(q̃)
8 if m_r[1].c ≥ τ_min then Y ← Y ∪ {(m_r[1].c, "rf", m_r)}
9 return arg max_{(c,·,m)∈Y} c
Spectral matching is always evaluated as a deterministic safety net. Learned models must clear τ_min to prevent confidently-wrong out-of-distribution predictions.
9/14

## Slide 10
Experimental Results
Aggregate accuracy
Component | Top-1 | Top-5
CNN — augmented validation (851 classes) | 98.6% | —
RF (PCA-120 + ExtraTrees-150) | 94.5% | 98.9%
Combined matcher — synthetic demo | 100% | —
Combined matcher — held-out RRUFF (n=6) | 83% | —
Per-mineral held-out RRUFF (auto mode, one specimen per mineral withheld from training)
Mineral | Matcher | CNN | Auto chose | Result
Quartz | 96.9% | 86.4% | matching | ✓
Calcite | 89.7% | 94.0% | cnn | ✓
Hematite | 91.6% | 90.1% | matching | ✓
Forsterite | 96.2% | 95.8% | matching | ✓
Aegirine | 86.2% | 97.0% | cnn | ✓
Magnetite | 76.6% | 90.1% | cnn | ✓ (matcher→Westerveldite)
10/14

## Slide 11
End-to-End Latency
Measured on a single laptop GPU (RTX 3050, 16 GB RAM). Budget τ ≤ 1 s — achieved at 160 ms median.
Pipeline stage | Median latency
File parse + linear interpolation | ≈ 45 ms
Cosmic-ray suppression + Savitzky–Golay + ALS baseline | ≈ 35 ms
Combined-metric spectral matcher (2,481 rows) | ≈ 25 ms
CNN forward pass (RTX 3050) | ≈ 12 ms
Candidate-set NNLS decomposition | ≈ 35 ms
End-to-end total | ≈ 160 ms
160 ms
end-to-end (budget: 1 s)
11/14

## Slide 12
Limitation: Scarcity of Diverse Reference Data
The fundamental bottleneck is the non-availability of curated, instrument-diverse Raman spectra with validated mineral labels.
System library and training set draw exclusively from RRUFF — a single-lab archive with its own instrument family, acquisition protocols, and specimen-selection biases.
RRUFF coverage is uneven: 2,456 mineral averages, many built from ≤3 raw specimens; rare minerals may have only 1 usable spectrum.
Consequence: behaviour on a novel instrument’s noise profile cannot be certified without an independent held-out test set from that instrument family.
Case study — Magnetite: 2 of 6 RRUFF specimens carry an instrumental cut-off artefact at 100 cm⁻¹, diluting the genuine 660–682 cm⁻¹ peak. Matcher returns Westerveldite; CNN recovers correct answer at 90%.
Path forward: multi-lab, quality-annotated spectral databases — an open data problem, not a modelling problem.
12/14

## Slide 13
Summary of Contributions
1
Grid-canonical preprocessing pipeline
Smoothing and baseline operators independent of the spectrometer’s native sampling; interpolation-first invariant
2
Combined-metric spectral matcher
s = ½ cosine + ½ second-derivative Pearson; each term vetos the other’s failure mode
3
663,539-parameter 1-D ResNet classifier
98.6% top-1 on 851 classes; 7-mode augmentation + Mixup; synthetic profiles appended to every matching class
4
Candidate-restricted NNLS decomposition
Converts underdetermined system (|ℛ|=2,481, P=1,951) into a ∼30-row over-determined, physically interpretable problem
5
Confidence-aware dispatcher (τ_min = 0.55)
Selects best identifier per query; spectral matching as permanent safety net; 160 ms end-to-end latency
13/14

## Slide 14
Live Demonstration
Uploading Quartz, Calcite, Pyrite, Gypsum spectra and a binary mixture
to the live Flask endpoint for real-time identification and NNLS decomposition.
160 ms
end-to-end
98.6%
CNN top-1
851
mineral classes
14/14